## Slide 1
Thermal Neutron Simulation From Different Geometries
Tushar Verma
Department of Chemical Engineering, Indian Institute of Technology Kanpur, 208016, India
tuhar22@iitk.ac.in, tusharverma218@gmail.com

## Slide 2
Introduction
Monte Carlo Simulation:
Computation technique to estimate possible outcomes of a process, using repeated random sampling.
Cross Section and Mean Free Path data for thermal neutrons (E ~ 25.3 meV):
 | Absorption | Scattering
 | λ (mean free path, cm) | 
H2O | 45.1766 | 0.6706
D2O | 24994.0175 | 2.8501
 | Absorption | Scattering
 | σ (cross section, barns) | σ (c.s., barns)
1H | 0.332 | 20.491
2D | 0.000506 | 3.390
8O | 0.000190 | 3.761
Table 1. JANIS cross section data for thermal neutrons.
Table 2. Calculated mean free path for thermal neutrons.

## Slide 3
Point Source @ (0,0,0): H2O
MC simulation for 5K neutrons, for 25 such data:
Scattering counts before absorption (aka n history): 68.2748 ± 0.7224
Mean of neutron distance: 6.2716 ± 0.0512 cm
Maximum neutron distance: 38.2243 ± 5.7061 cm
Maximum neutron counts

## Slide 4
Point Source @ (0,0,0): D2O
MC simulation for 5K neutrons, for 25 such data:
Scattering counts before absorption (aka n history): 8795.1912 ± 138.0917
Mean of neutron distance: 308.5265 ± 2.8019 cm
Maximum neutron distance: 1793.4059 ± 218.9170 cm
Maximum neutron counts

## Slide 5
Cylinder Source @ (h = 4cm z:[-2,2], d = 0.5 mm): H2O
MC simulation for 5K neutrons, for 25 such data:
Scattering counts before absorption (aka n history): 68.3475 ± 1.0078
Mean of neutron distance: 6.2818 ± 0.0613 cm
Maximum neutron distance: 37.5690 ± 3.9512 cm
Maximum neutron counts

## Slide 6
Cylinder Source @ (h = 4cm z:[-2,2], d = 0.5 mm): D2O
MC simulation for 5K neutrons, for 25 such data:
Scattering counts before absorption (aka n history): 8771.1276 ± 117.2476
Mean of neutron distance: 308.1507 ± 3.1943 cm
Maximum neutron distance: 1819.5574 ± 241.4102 cm
Maximum neutron counts

## Slide 7
Spherical Source @ (r = 1cm & c:[0,0,0]): H2O
MC simulation for 5K neutrons, for 25 such data:
Scattering counts before absorption (aka n history): 68.4373 ± 0.9366
Mean of neutron distance: 6.2874 ± 0.0555 cm
Maximum neutron distance: 37.5249 ± 5.0371 cm
Maximum neutron counts

## Slide 8
Spherical Source @ (r = 1cm & c:[0,0,0]): D2O
MC simulation for 5K neutrons, for 25 such data:
Scattering counts before absorption (aka n history): 8771.5681 ± 146.0955
Mean of neutron distance: 308.1092 ± 3.6943 cm
Maximum neutron distance: 1925.7930 ± 313.9405 cm
Maximum neutron counts

## Slide 9
 | N History | Mean N Distance | N History | Mean N Distance
Source ↓ | H2O |  | D2O | 
Point | 68.27 ± 0.72 | 6.27 ± 0.05 cm | 8795.19 ± 138.09 | 308.53 ± 2.80 cm
Cylinder | 68.35 ± 1.01 | 6.28 ± 0.06 cm | 8771.13 ± 117.25 | 308.15 ± 3.19 cm
Spherical | 68.44 ± 0.94 | 6.29 ± 0.05 cm | 8771.57 ± 146.09 | 308.11 ± 3.69 cm
Results & Discussions:
Inferences:
Moderator plays a dominant role in neutron transport. D2O enables over 100x more scatterings and 50x longer travel than H2O.
The geometry of the neutron source has minimal effect on the overall scattering statistics and mean travel distances in a homogeneous medium.
The results align with theoretical expectations from cross-section and mean free path data derived from JANIS.